Tasks:
- Identify where the states are defined: how many, signal names, values, etc.
  - 20 signals
  - Self defined
    - i2c_state
      - i2c_st_ready,
      - i2c_st_start,
      - i2c_st_address
      - i2c_st_sl_ack1
      - i2c_st_sl_ack2
      - i2c_st_wr,
      - i2c_st_rd,
      - i2c_st_ma_ack,
      - i2c_st_stop
    - i2c_next_state
      - i2c_st_ready,
      - i2c_st_start,
      - i2c_st_address
      - i2c_st_sl_ack1
      - i2c_st_sl_ack2
      - i2c_st_wr,
      - i2c_st_rd,
      - i2c_st_ma_ack,
      - i2c_st_stop
  - Boolean
      - Ture
      - false
    - i2c_bit_counter_reset
    - i2c_bit_counter_max
    - i2c_bit_counter_tick
    - i2c_time_counter_reset
    - rd_data_tick
    - rd_data_end
  - std_logic_vector(7 downto 0)
    - i2c_time_counter_q
      - 00000000 to 11111111
    - i2c_time_counter_next
      - 00000000 to 11111111
    - i2c_int_address
      - i2c_address i2c_rw
    - i2c_rd_data
      - read of sequence of sda_in
  - natural
    - i2c_bit_counter_q
      - range 0 to 7
    - i2c_bit_counter_next
      - range 0 to 7
  - std_logic
      - 0/1
    - sda_tris_int
    - sck_tris_int
    - i2c_busy_int
    - ack_tick_int
- In “SYNC_PROC”: four types of memory elements: state register, counters, data register and output buffers. Identify how these are implemented
  - State
    - i2c_state
      - reset to i2c_st_ready on reset mode
      - set to be the i2c_next_state on non-reset mode
  - counter
    - i2c_time_counter_q
      - reset to 00000000 on reset mode
      - set to be the i2c_time_counter_nexton non-reset mode
    - i2c_bit_counter_q
      - reset to 00000000 on reset mode
      - set to be the i2c_bit_counter_next on non-reset mode
  - data register
    - i2c_rd_data
      - reset to 00000000 on reset mode
      - shift left and set sda_in in to the register
  - buffers
    - sda_tris_int
    - sck_tris_int
    - i2c_busy_int
    - ack_tick_int
      - glitch canceling on output
- Implementation of Boolean signals before next process to increase readability of if-statements
- Separate process for output decode; special arrangement for implementation in hierarchical design.
- Task: Draw a state diagram for the states implemented in this code